Escalator	Repair

& REBUILD

THEORY OF  OPERATION

Prior  to attempting repair  or adjustment of the escalator  it is  important to understand its purpose and function.

The  escalator ac ce pts     the  cdin  thereby  allows  the  mechan- ism    to be operated.	It  is  designed to a cc ep t  the correct denomination,  reject or not  accept  the  wrong denomination, provide a visual  indication  of coins recently  played and then

deposit the  coin into  the appropriate  area. 	(The coin  tube).

The  mills  type escalator  functions by the  following  sequence of actions:

.     Coins of  the    corre ct size  or smaller can  be

inserted  in the hole.

The  coin slides  down a  path  by gravity  past  a magnet assembly  which  has  been  adjusted to  allow the  correct size  coin to  pass.

Smaller coins are  sent  or  "shunted" to a different path  and fall out  through a space provided  on the

far left    side	(facing the escalator  front).

The  magnet also  causes  ferrous  slugs to  be "shunt­

ed"   down the different path .

.   The   correct  coin howeve r, passes the magnet,	con­ tinues  on  the correct  path  and lands directly  in front  of the finger  of    the coin detector  lever

(P    figure  1)  .  ,

The coin  is  prevented  from continuing across the escalator by the  first "tooth" of  the  coin hold­ ing  bar   (E).

A  small cut  in the face plate  directly  in front of    the coin detector  finger  also  acts  to  reject smaller  coins.	They  are  pushed out thru  the  front by  the finger  and slide  down  the slug chute cover assembly   (AA).

If  when the coin detector  lever is moved forward by  the coin detector  operating  l ever the  finger feels  a coin, and if  the length of the finger is adjusted  correctly,	the  mechanism will be  al low­

ed to operate.

C 	D

F ic, ure.	3

o-----

- -  -  - �  ....

0	o	o

0

Faq u�e	4

-3-

If  the machine is not used extensively twice a  year  is

suggested.

The  escalator may  be  cleaned by washing with  a  brush using trichloraethylene  or a  s i m i lar    solvent.	It may then  be brushed with a  degreasing  detergent  and washed off  with very hot  water.	The  escalator  should be  dried with forced a ir  or freon TF   spray  and lubricated.

LUBRICATION:

The  entire  rear of the e s ca l ato r may be  sprayed with  a good machine  oil  such as 3   in 1     spray, 	or a  drop of oil placed  on  every  moving j o i nt .	Each  moving  part  should then  be move d  to  insure  free  movement. 		A    slight  appli­ cation of pe t r o le um  jelly  or lubriplate  may  be  applied

between the  coin  advance  bar  (D)     and the body of  the

escalator.	The  c o in track  should be kept  free  of  lub­

ricant as  i t can  cause  "hanging"�

ALL  SLIDING   OR PIVOTING   PARTS MUST BE  WO RK I N G    FREELY MAGNET ADJUSTMENT:

The magnet is  factory adjusted however,·should  it ever

be necessary  to replace  or 	the magnet,	first move

it over  to t he right  j ust 	to block the passage of  a  coin.	Fasten it loosely  in place . 	Wh ile  the   coin

is  still touching  the Magnet, move  t he Magnet slowly  to

the  left until the  coin passes  through with ease . 	Tighten the  screw which holds   the  Magnet in place. 	Check your adjustment  by playing a  steel  slug to see if  it is  drawn

to the return track.

TROUBLESHOOTING   ESCALATOR  PROBLEMS

Troubleshoo t ing     t he  escalator is  divided i nto  two parts.

The  first part  establishes  the escalator to be  operative, or inoperative,  separately  from    the  mechanism.	The  sec­ ond  part  describes problems that  may  occur  when the  es­ cal ator is  activated  by the  mechanism.

CHECKOUT  OF   THE  ESCALATOR   WITHOUT 	MECHANISM

•     Remove     the  mechanism from the cabinet.

While observing the  escalator,  deposit a coin  and see if it  lands  j ust     in front of the detector  bar finger.

A'I

Iff

AA    c:-y

AS

Fi gvre	I

-5-

Establish this operation  in your mind.	Observe each  function as  it occurs and  establish  the 1function    of each part. 	By  now, you  s houl d  understand  the  escalator.

Most  problems  occur when the  escalator  is  interfaced with the mechanism. 	The  following paragraphs  establish problems  that may occur  when    the  escalator is worked  with  the mechanism.

TROUBLESHOOTING   THE  ESCALATOR   COMBINED  WITH  THE  MECHANISM

.   Visually  inspect'the    mechanism  after insertion of    the  mechanism into the cabinet.	Assure that:

.  The  coin  advance bar  operating  lever	(A   figure

3)	is "Hooked"  over the lip  of the  coin  ad­

vance bar  lever 	(F,  Fi g ure   1).

The  coin detector lever, 	(P    Figure l) 	is not being  pushed  forward  by the coin detector operating  lever	(C,Figure 3).

The  coin detector  operating lever 	(C   Figure

3) 	is  not rubbing against  the coin detector

lever  (   P,figure  1)   end  guide .

The  check  detector  operating arm   (B,	Figure

3)	is not p ushing    against  the check detector lever  (S,  Figure  1)

The  next  step requires activation  of  the  mechan­ ism however, a technique to stop the timing cycle will be applied  to  slow down the   cycle. 	This

will facilitate observation  of  the sequence of

events .

•   Place a  screwdriver handle,	or   similar  item

next  to  the  clock  fan  to   stop its rotation .

. 	I ns ert    a  coin in  the escalator

From the rear� observe that  the  coin  lands directly in front  of  the coin  detector finger.

-7-

Did the  coin advance  b ar    locking lever  lock the

coin  advance bar into  the left position?

If the  answers to  the  above questions  was yes, continue on  to   the following steps.	If the answer was no,   go  back and review the sequence of  oper­ ation to  determine where the problem may  l ay .

.  Remove the screwdriver  handle from the clock  fan and  use   a finger to  reduce the speed  of the clock. As  the  mechanism cycle continues,  observe  the following:

.   The coin  advance bar operating lever  strikes

the pertruding  bar  of  the coin bar release  lever

(H.  Fig   1)  and  moves  it up.

The hook next  pushes   up  on  the pertruding  bar of the coin  advance  bar locking  lever  releas­ ing  the coin advance  bar .

.  The  coin  advance bar  slides  or snaps back to

the  right  hand position .

•    With  the  hook  completely returned to  its  upper. position  (upon completion  of the  mechanism cycle) the  coin detector bar  and check  detector  lever

are fully against their  back  stop.

If all the properly. repeat  the ing;

above actions  occur,  the escalator  is working However.  if the  action  does not seem proper, cycle  as  outlined above and observe the follow-

.As  the  coin  advance bar  operating  lever rises, observe  if there  is  resistance c au se d by rubbing against  the inside handle  lever if so,	this must be  resolved •

• The operating  parts on  the  side  of the  mechanism should be  lubricated.	If  lubrication has just been accomplished and  the  machine  ha�  been out of

use for  a prolonged period  of time,  the  lubrication

mus t  be "worked in" by repeated  use.

-7-

Did the  coin  advance bar locking  lever lock the coin advance bar into  the left  position?

If  the answers  to  the  above questions  was  yes, continue on  to  the following steps. 	I£  the  answer was   no,  go back and review  the  sequence of oper­ ation  to  determine where the problem may lay .

•     Remove   the screwdriver  handle  from the  clock  fan and use   a  finger  to  reduce the  speed of  the  clock. As the  mechanism  cycle continues,  observe  the

following:

The  coin  advance bar operating lever strikes

the pertruding  bar of the coin bar release  lever

(H.  Fig   1)  and  moves it up.

The hook next  pushes  up on  the pertruding  bar of  the  coin  advance bar  locking  lever releas­ ing the  coin advance  bar .

•    The coin  advance  bar  slides  or  snaps back to

the right hand position .

•    With  the hook compl¢tely returned to  its  upper­ position  ( upon completion  of  the  mechanism cycle) the  coin  detector  bar and check detector lever

are fully  against their back stop.

If all the properly. repeat  the ing;

above actibns  occur,  the  escalator  is working However,  if  the action does not  seem proper, cycle as outlined  above  and  observe the  follow-

.As  the  coin advance bar operating  lever  rises, observe if  there is resistance caused by rubbing against the inside handle  lever if so, 	this must be resolved •

. The   operating  parts  on the side of  the  mechanism should  be  lubricated. 	If lubrication  has  just been  accomplished and the  machine has been out  of

use for a  prolonged period of time, the lubrication

must   be "worked in"  by  repeated use .

-5-

Establish  this  operation in your mind.	Observe each function as it occurs and  establish  the function of each part.	By  now, you should understand  the escalator.

Most problems  occur  when the escalator is interfaced  with  the mechanism. 	The  following paragraphs  e s t ab l i s h problems  that may  occur when  the escalator is worked  wi th the  mechanism.

TROUBLESHOOTING    THE  ESCALATOR   COMBINED  WITH   THE  MECHANISM

.   Visually  inspect  the mechanism  after  insertion

of the  mechanism into  the cabinet.	Assure that:

.    The  coin advance bar operating  lever 	(A   figure

3)	is "Hooked" ove r  the  lip of the  coin ad­

vance bar lever	(F, Figure 1).

The  coin detector  lever, 	(P  Figure   1)	is not being pushed forward  by t he  coin detector operating lever  (C,Figure 3).

The coin detector  operating lever	(C    Figure

3)   is not rubbing against  the coin detector lever  (   P,figure 1)  end guide.

The  check  detector operating  arm  (B,	Figure

3)	is  not pushing against the  che ck  detector

lever  (S,  Figure  1)

The  next step requires activation  of  the  mechan­ ism however, 	a  t e chni que to  stop  the  timing cycle will be applied  to  slow  down the  cycle. 	This

will facilitate  observation  of  the  sequence of events .

•    Place   a  screwdriver handle,	or  similar  item

next  to  the  clock fan to  stop its rotation .

.	Insert a  coin in  the    escalator

From the  rear,  observe that  the  coin  lands

directly in front of the coin detector finger.

.,

c-.Q·.

c..,.

-

(\)

1

I

- 3 -

If t he machine is  n ot    used extensive ly  twice  a  year is suggested.

The  escalator may    be  cleaned  by washing with a  brush using trichloraethifl ene or a  similar  solvent. 	It  may then  be brushed with a  degreasing detergent  and washed off  with very  hot  water. 	The escalator should  be  dried with forced air  or  freon TF   spray  and lubricated.

LUBRICATION:

The  entire re ar of the escalator  may be sprayed with a good  ma ch i ne oil  such as 3   in 1   spray, 	or   a  drop of oil placed  on every  mov i n g   joint.	Each  moving  part  should then  be moved to insure  free  movement. 		A    slight ap pl i ­ cation  of petroleum jelly  or l ubrip l ate    may be  applied

between  the    coin  advance b ar 	(D)    and the  body of  the

escalator.	The coin  track  should be kept  free  of  lub­

r i cant    as it  can cause "hanging".

ALL SLIDING   OR  PIVOTING   PARTS  MUST BE  WORKING FREELY MAGNET ADJUSTMENT:

The  magnet   1s  factory adjusted however,·should  it  ever

be necessary  to  replace    or  a d j us t the magnet,	first move

it o ver    to the right    just  far enough to block the passage

of a  coin.	F as te n it  loosely in place.	Whi le     the coin

is still touching    the Magnet,   move the Magnet slowly to

the left    until the coin  passes  t h ro u gh with  ease . 	Tighten the  screw wh i ch hol ds  the  Magnet in p l a ce .	Check  your adjustment  by playing a steel  slug  to see if it is  drawn

to  the return  track.

TROUBLESHOOTING   ESCALATOR   PROBLEMS

Troubleshooting the  e s c a l a t or     is  divided into  two  parts. The  first part establishes the e s c al a tor     to be operative, or inoperative,  separately  from the  mechanism.	The sec­ ond  part describes prob lems     tha t may  o cc ur  when the  es­ calator is activated by the  mechanism.

CHECKOUT   QF  THE  ESCALATOR  WITHOUT  THE   MECHANISM

.   Remove   the mechanism    from  the cabinet.

While  o bs e rv i n g  the escalator,  de p o s it a  coin and

see if it  lands just  in front of the detector bar

finger.

('

C 	D

F ic., vr-e. 	3

-  -   -  -

--  ..............

0

THEORY  OF    OPERATION

Prior to  attempting r ep a ir  or adjustment of the escalator  it is important to understand its  pu rpos e  and function.

The  escalator  accepts the coin thereb y allows   the  mechan- ism    to  be operated. 	It is designed to accept  the correct denomination, reject  or not accept the wrong denomination, provide a visual  indication  of coins recently played and  then

deposit  the coin into the  appropriate area. 	(The coin  tube).

The mills  type escalator  functions by the  following  sequence

of actions:

Coins of the correct  size or smaller can be

inserted in the ho le.

The  co i n  slides  down a  path  by gravity past  a magnet assembly  which has  been  adjusted to  allow the  correct  size  coin to pass.

Smaller coins  are sent  or  "shunted" to a different path  and fall out  through a  space provided on the far left  side	( facing the escalator  front).

The magnet  also  cause s ferrous  slugs  to  be  "shunt­

ed"   down th e different  path .

•    The correct  coin however, passes  the magnet, 	con­ tinues  on  the correct path and lands directly  in front  of the f inger    of the  coin   de tec t o r  lever

(P    figure  1)  .

"

"

The  coin  is prevented  from continuing  across  the

escalator by the  first

ing  bar 	(E).

t o o th	of  the  coin  hold­

A   small  cut  in the  face  plate directly in front of    the  coin detector finger  also  acts  to  reject smaller coins. 	They are  pushed out thru the front by  the  firtger  and  s li de  down  the slug  chute cover assembly   (AA).

If  when the coin  dete c t o r  lever is moved  forward by the  coin  de t e c tor   operating lever the finger feels  a coin,	and if  the  length  of  the finger is adjusted correctly, 	the  mechanism will  be allow­ ed to operate.

Escalator	Repair

& REBUILD