2-11-03

New features SW  Z 4.0.0

- Possibility to print a report by connecting the printer DP42A (Custom Engineering) to the ZIP unit

- Possibility to reset the Data once collected.

- Possibility to store hystorical data in the RAM expansion (RAM is compulsory).

- Possibility to transfer the RAM expansion to another ZIP CPU in order to continue the data collection (when the ZIP CPU is damaged).

- Collection of Historical data using DATA KEY.

### 1 How to print the Report

Enter “OTHER  PARAMETERS”,   “AUDIT  MODE”,  “PRINTER

Connect the printer to the ZIP CPU using the RS232 cable and after 2 seconds the printer will print the statistics.

Press Print for additional reports.

2 Data printed

LOADING : total loadings using  programmer  or charge key.

This because the software developed for this customer does not allow to load money in the key using the VMC.

SALES  WITH  CASH / WITH  KEY:

- number of sales can reach up to 999999, ( 65535 with the  ZIP standard ).

- 10 selections .

3 How to reset the data once collected

Dopo la stampa i dati presenti nel Report, che nel seguito sono chiamati  “Dati Parziali”, possono

essere azzerati o meno.

The resetting is possible only if the parameter “RESETTING” (“OTHER  PARAMETERS”, “AUDIT  MODE”) is set to ON.

- Press 3 times within 2 seconds “PRINT”;

- “RESET  AUDIT ?”, “<PRINT> to confirm”;

- Press “PRINT” within 5 seconds otherwise the reset will not be performed “RESET NOT PERFORMED”.

- After the reset the printer will print “RESET OK”.

After the reset the data are added to “CUMULATIVE COLLECTIONS”.

4 Collection of Historical data using DATA KEY

The data once collected are added to the ones stored in the memory.

Historical data can be collected using a Data-Key.

In order to print the data you need a PC Interface software ver. “PSCP 1.1.0 P” BOX32 ver. 1.2.0.

See below the format.

To reset the hystoricaldata use the programmer (menù statistics protected by a password).

#### 5 Loading the software

- Use the Flash Programmer.

- INIZIALISATION of the system

- RESET the hystorical data

- Collect the data using the Data Box

Now the ZIP unit is ready.

6 PRINTER

The batteries can work upo to  3 hours.

The charging period = 8 hours.

7 Wall Loader

The report is the following: