-   English   -

PC Interface

Release 2.0 -  May 2004

The manufacturer reserves the right to modify, without prior notice, the characteristics of the equipment described in this publication; and further declines to accept any responsibility for any inaccuracies contained in this publication which can be ascribed to printing and /or transcription errors.

All instructions, drawings, tables and information contained in this publication are confidential and can neither be reproduced, completely or in part, nor be transmitted to third parties without the written permit of the Manufacturer,  who has the sole ownership.

ENGLISH

# ZIP PC INTERFACE

# Operating and Installation Manual

INTRODUCTION

This technical documentation is part and parcel of the machine. Therefore, it must always follow the machine when it is moved or when the ownership is transferred, so that different operators may be able to consult it.

Before installing or using the machine, it is necessary to carefully read and understand the instructions contained in this manual, as they offer important information for safe installation, use and maintenance.

Any operation must be carried out exclusively by personnel who have a specific knowledge of the machine functions.

IDENTIFICATION OF THE MACHINE AND ITS CHARACTERISTICS

Every machine is identified by its own MODEL and SERIAL NUMBER, indicated on the rating plate attached to the cabinet.

This plate is the only acknowledged by the manufacturer as identification of the machine and carries data which safely gives technical information supplied by the manufacturer.

It is, therefore, recommended that this plate be neither damaged nor removed.

MODEL

MODEL                     958995

SERIAL N°            41900001                        PRODUCTION BATCH

18/24 VAC  50/60 Hz 150mA

manufactured by

TENSION-FREQUENCY-RATED CURRENT

PRODUCER

WARNING FOR SCRAPPING

Whenever the machine is to be scrapped, the laws in force regarding environment protection should be strictly observed. Ferrous and plastic materials and the like are to be disposed of in the authorised areas only.

TECHNICAL SPECIFICATIONS

POWER SUPPLY VOLTAGE					:	18/24VAC

(Through an external transformer,

supplied with the PC interface and

connected to the power supply)

POWER SUPPLY FREQUENCY					:	50/60 Hz

RATED CURRENT							:	150 mA

DIMENSIONS W x H x D (mm)					:	100 x 182 x 190

MAIN FEATURES

- Possibility of displaying and printing the statistical data retrieved with the Maxi Key, the Data Key, the Data Box, or with the palm-top PC PSION.

- Possibility of programming the keys/cards, defining: Sales Keys, Free Sales Keys, Discount Keys (3 levels). It is also possible to operate in the Service Keys (Maxi Key, Data Key).

REQUIREMENTS OF THE SYSTEM TO WHICH CONNECT THE PC INTERFACE

- Personal computer IBM compatible, Pentium III or above, with at least 128 MB of RAM.

- CD-ROM.

- Correctly installed Mouse.

- A fully compatible printer.

- Microsoft Windows 98 or above.

- A free serial port (COM 1 / COM 4)

INSTALLATION OF THE SOFTWARE BOX32 AND KEYCARD

The PC interface is supplied with a CD-ROM named KeyCard Tools, including the Box32 and KeyCard software, and with an additional CD-ROM including the drivers for USB.

For the installation in the PC of the Box32 and KeyCard software, proceed as follows: (Windows must already be installed)

1) Switch the PC on and start Windows.

2) Insert the CD-ROM named KeyCard Tools.

3) Choose the folder with the application you want to install (KeyCard first and then Box32).

4) Open the folder, start the program setup.exe and follow the instructions.

5) Connect the PC Interface, by means of the cables supplied with the unit, as shown in Fig. 1

The folder KeyCard Tools, containing the sub-programs BOX32 and KeyCard, is created in the PC during the previously described installation procedure. These sub-programs respectively concern the management of statistical data and of the keys/cards.

# ! WARNING

If the PC does not have standard serial portals but only USB portals, it is necessary to connect the Interface by means of the serial/USB adaptor cable which is supplied with the equipment.

In order to use this cable it is necessary to install the USB driver in the PC, following the instructions contained in the KeyCard Tools CD-ROM.

Fig. 1

DESCRIPTION OF FIELDS IN THE SW KEYCARD (SEE FIG. 2)

1) Pull-down menu that contains the following options:

Settings / read / modify

Settings / automatic formatting

Settings / bonus: it allows setting the fields related to the bonus mode

Settings / operator code: allowing the setting of the operator code (non displayable).

2) Allowing the selection of “read / modify” or “automatic formatting” modes (to start with “automatic formatting” mode, insert a key/card and follow the instructions displayed at the bottom of the window).

3) Write command for a single key (enabled choosing “read / modify”).

4) Command to load the previously saved default data in field 9).

5) Command to store the data of field 9) as default data.

6) Black List command to create a Black List up to 500 keys/cards (see instruction “Special Keys”).

7) Field of values read from the key/card.

8) Selection of the type of key/card to be programmed: sales and free sales.

9) Field of values to be written into the key/card.

10) Selection of the discount level to set into the key/card: level 0, level 1, level 2, level 3.

11) Field of bonus.

Fig. 2

MANAGEMENT OF DATA FOR THE KEYS

- System configuration

Enter the File/configuration menu and select the desired parameters "serial portal, acoustic alarm, language and decimal point".

# ! WARNING

In the same menu it is possible to insert a password which, if inserted, will be requested each time the program is started.

To modify this password it is necessary to install the KeyCard program again.

- Selection of the Operator Code:

Each Vending Operator will have to enter the desired operator code (Settings/Operator Code) into the keys/cards replacing the default code (00000001).

# ! WARNING

If a key belonging to another vending operator is inserted in the PC Interface, the message “Wrong Operator Code” will be displayed and the key/card cannot be read or written.

# Text boxes

11

1

10

8

2

6

5

4

3

9

7

Operating and Installation Manual