- English -

Release 1.1 -  January 2004

TECHNICAL DATA

Power supply voltage:                                                			     18-28V AC +/-10% 50/60Hz

Key reader: r.f. Operation 125 KHz                             			     Hole dimensions = 35 mm.

The manufacturer reserves the right to modify, without prior notice, the characteristics of the equipment described in this publication; and further declines to accept any responsibility for any inaccuracies contained in this publication which can be ascribed to printing and /or transcription errors. All instructions, drawings, tables and information contained in this publication are confidential and can neither be reproduced, completely or in part, nor be transmitted to third parties without the written permit of the Manufacturer,  who has the sole ownership.

INSTALLATION

Operations to be carried out by qualified personnel with the equipment disconnected from the power supply.

! WARNING before any operation tests ensure that all equipment is properly and efficiently connected to earth.

ZIP reader is supplied as in the picture.

The metal sheet can be removed or fixed with the reader

depending on the situations.

# -  CASE1  -

Door of the vending machine (1) in plastic material: fix the reader with the metal sheet

###### - CASE 2 -

Door of the vending machine (1) made of painted or galvanized metal sheet with a pre-cut hole as in the picture: fix the reader with the metal sheet.

## - CASE 3 -

Door of the vending machine (1) made of painted or galvanized metal sheet with a 35 mm hole for the reader (made according to the hole design kit): remove the metal sheet.

# Text boxes

Installation manual