-   English   -

Portable Revaluation Unit

Release 1.0 -  May 2004

The manufacturer reserves the right to modify, without prior notice, the characteristics of the equipment described in this publication; and further declines to accept any responsibility for any inaccuracies contained in this publication which can be ascribed to printing and /or transcription errors.

All instructions, drawings, tables and information contained in this publication are confidential and can neither be reproduced, completely or in part, nor be transmitted to third parties without the written permit of the Manufacturer,  who has the sole ownership.

ENGLISH

# ZIP PORTABLE REVALUATION UNIT – Keys / Cards Desktop Charger

# Operating and Installation Manual

INTRODUCTION

This technical documentation is part and parcel of the machine. Therefore, it must always follow the machine when it is moved or when the ownership is transferred, so that different operators may be able to consult it.

Before installing or using the machine, it is necessary to carefully read and understand the instructions contained in this manual, as they offer important information for safe installation, use and maintenance.

Any operation must be carried out exclusively by personnel who have a specific knowledge of the machine functions.

IDENTIFICATION OF THE MACHINE AND ITS CHARACTERISTICS

Every machine is identified by its own MODEL and SERIAL NUMBER, indicated on the rating plate attached to the cabinet.

This plate is the only acknowledged by the manufacturer as identification of the machine and carries data which safely gives technical information supplied by the manufacturer.

It is, therefore, recommended that this plate be neither damaged nor removed.

MODEL

MODEL                     958996

SERIAL N°            41400001                        PRODUCTION BATCH

18/24 VAC  50/60 Hz 150mA

manufactured by

TENSION-FREQUENCY-RATED CURRENT

PRODUCER

WARNING FOR SCRAPPING

Whenever the machine is to be scrapped, the laws in force regarding environment protection should be strictly observed. Ferrous and plastic materials and the like are to be disposed of in the authorised areas only.

TECHNICAL SPECIFICATIONS

POWER SUPPLY VOLTAGE 						:	18/24VAC

POWER SUPPLY FREQUENCY						:	50/60Hz

RATED CURRENT				                   	    		:	150 mA

DIMENSIONS  W x H x D (mm.)						:	100 x 182 x 190

# MAIN FEATURES

- Possibility of charging the keys or displaying the available credit.

- Possibility of programming the keys, by means of the programming terminal, similarly to a payment system.

- Possibility to store the statistics of the charged credit.

- The unit is protected from use by unauthorised persons.

INSTALLATION

- Plug in the transformer into a 220/240 VAC socket outlet.

- Insert the jack fitted at the end of the transformer cable into the socket located at the back of the portable key charger.

- Turn the unit on by using the switch located on the front panel.

- Check that the led of the ZIP module is illuminated by a green light.

- Enter the codes and the type of charge to be used into the machine.

! WARNING

Installation and the following maintenance operations should be carried out by qualified personnel only, who are trained in the correct use of the machine according to the standards in force.

REVALUING THE KEY WITH THE BUTTON

- Set the value of the charge in the menu MACHINES / KEY CHARGER: PORTABLE / RECHARGING VALUE.

- Program the menu OTHER PARAMETERS / CHARGE KEY = OFF.

- Programme OTHER PARAMETERS / SECURITY KEY / ON/OFF, depending on whether you want to enable machine protection or not.

- If the SECURITY KEY parameter has been set to ON, after been switched-on, the display will read “OUT OF ORDER” until a charge key is inserted with the correct operator code. When the key is removed the machine is ready to operate.

- The credit to be transferred to the key is increased by pressing the “ + ” key (situated at the centre of the front panel). This can also be done after having inserted the key into the unit.

- Insert the Sales Key: the value on the display will be added to the key.

- If a Charge Key is inserted, the display will indicate the number of charges and nothing more, even if the button is pressed.

REVALUING THE KEY WITH THE CHARGE KEY

- Program the menu OTHER PARAMETERS / CHARGE KEY = ON.

- Insert a Charge Key: the number of available charges and the value of the charge will appear on the display.

- Press the button: a charge is deducted from the key and the display indicates the value of the charge.

- Remove the Charge Key and insert the Sales Key: the value on the display will be added to the key. The display indicates the new credit of the Sales Key.

- If no Sales Key is inserted, after 30 seconds the charge is “erased” and is added to the value of the diagnostics statistics S58 (E11).

CHECKING THE CREDIT

- Program the menu OTHER PARAMETERS / CHARGE KEY = OFF.

- Program the menu MACHINES / KEY CHARGER: PORTABLE / RECHARGING VALUE = 0

(pressing the button will not increase the credit).

- When a Sales Key is inserted the credit appears on the display but this cannot be modified.

- When a Charge Key is inserted the number of charges appears on the display but this cannot be modified.

ERASING THE CREDIT IN THE KEY

- Insert the Sale Key to be erased.

- Press key “ – “ (located on the right side of the front panel) and keep it pressed until the display reads “ERASING” – “DO YOU CONFIRM ?”

- Press key “ + “ (central) to confirm. If no key is pressed within 5 seconds the function is exited.

The credit erased from the keys using this function will go under the item indicated by the display with the wording “Credit Erased” under item “Overpay” on the statistics print-out.

! WARNING

If the push-button operating mode is enabled, the machine must not be left unattended, as anyone would be able to use it. The “SECURITY KEY = ON” operating mode allows you to avoid this problem. In all cases, the unit must be switched off after use.

DISPLAY OF CHARGED AND ERASED CREDIT

By pressing key “ + “ for more than 3 seconds, it is possible to enter the following display modes:

“Revaluation”, “Failed Revaluation” and “Credit Erased”. After having entered this mode, these 3 statistical data are displayed one after the other when pressing the button.

To exit this mode, keep the button pressed for more than 5 seconds or wait 20 seconds without effecting other operations.

When a statistics collecting operation is effected, the following data is reported respectively in the statistics:

      - “TOTAL LOADING”  Programmer or Charge Keys.

      - “FAILED LOADING USING CHARGE KEY”.

      - “OVERPAY”.

! WARNING

Data collection causes all data to be cleared.

# Text boxes

Operating and Installation Manual