LAYOUT L15.

PRODUCT TABLE.

POSIT.

PRODUCT

N° DOSING

SETT. DOS.

(gram./sec.)

N° ELECTRO.

SETT. EV

| (cc/sec.) |
| --- |
| 1 | Whitener / Milk | 1 | 1,5 | 1 | 9 |
| 2 | Sugar | 2 | 2,3 | 1 | 9 |
| 3 | Fresh Brew 1 | 3 | 1,7 | 2 | 16 |
| 4 | Fresh Brew 1 |
| 5 | Coffee Ins. / Soup * | 4 | 0,6 / 2,5 * | 4 | 10 / 15 * |
| 6 | Fresh Brew 2 | 6 | 1,7 | 5 | 14 |
| 7 | Fresh Brew 2 (C2) | 8 | 1,7 | 5 | 14 |
| 8 | Chocolate | 7 | 3,0 | 6 | 9 |
| / | Hot Water | / | / | 3 | 20 |
| / | Carbonated Water | / | / | 7 | 17 |
| / | Still Water | / | / | 8 | 16 |

KEYBOARD SELECTION L15.

| Strength - | ( | Strength + | ( |
| --- | --- | --- | --- |

SELECTION

SUGAR

N.

EX. SUGAR

N.

NO SUGAR

| N. |
| --- |
| Coffee Fresh Brew Black | 17 | 18 | 19 |
| Coffee Fresh Brew White | 21 | 22 | 23 |
| Coffee Fresh Brew Ex. White | 24 | 25 | 26 |
| Chocolate | -- | -- | 27 |
| Soup * | -- | -- | 28 * |
| Hot Water | -- | -- | 29 |
| Coffee2 Fresh Brew White | 31 | 32 | 33 |
| Coffee2 Fresh Brew Ex. White | 34 | 35 | 36 |
| Coffee Instant Black | 37 | 38 | 39 |
| Coffee Instant White | 41 | 42 | 43 |
| Coffee Instant Extra White | 44 | 45 | 46 |
| Coffee2 Fresh Brew Black | 47 | 48 | 49 |
| FB Tea White | 51 | 52 | 53 |
| FB Tea Extra White | 54 | 55 | 56 |
| Fresh Brew Tea Black | 57 | 58 | 59 |
| Coffee Fresh Brew Cappuccino | 61 | -- | 62 |
| Coffee Fresh Brew Espresso | 63 | -- | 64 |
| Coffee Fresh Brew EspressoChoc | 65 | -- | 66 |
| ChocoMilk | -- | -- | 67 |
| Instant Cappuccino | 71 | -- | 72 |
| Instant EspressoChoc | 73 | -- | 74 |
|  | STILL |
| CARBONATED |
| Chilled Water | 81 |
| 84 |
| Orange ( Syrop 1 ) | 82 |
| 85 |
| Lemon (Syrop 2 ) | 83 |
| 86 |

* When it takes the place of the Coffee Instant with the Soup, and vice versa, is necessary disable the selections of the powder to replace and train those of the new, therefore modify of the value of setting of the doseur and electrovalve. correspondent like suitable in the table product.

* Quando si sostituisce il Coffee Instant con il  Soup, e viceversa, e’ necessario  disabilitare le selezioni della polvere da sostituire ed abilitare quelle della nuova, quindi  modificare del valori di taratura del dosatore ed elettrov. corrispondente come indicato nella tabella prodotti.

PRESELECTION L15.

PRESELECTION

(N.)

DOSE VARIAT.

| DESCRIPTION |
| --- |
| Strength - | -10 % | Reduces the powder of Coffee/Tea (3 step). |
| Strength + | +10 % | Increase the powder of Coffee/Tea (3 step). |
| Extra Sugar | + 66% | Increase the dose of sugar to 66% |
| No Sugar | - 100% | Reset the dose of sugar of the selection |

SELECTION L15.

SELECTION

(N.)

WATER DOSES

SUGAR

(to door)

POWDER DOSES

Fresh Brew Black

( 17 – 18 – 19 )

Coffee FB

110 cc

Coff. FB

9,0 gr.

Sugar

60 cc (tot. 170 cc)

Sugar

5,3 gr.

Fresh Brew White

( 21 – 22 – 23 )

Coffee FB

110 cc

Coff. FB

9,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

1,5 gr.

Sugar

5,3 gr.

Fr. Br. Ex.White

( 24 – 25 – 26 )

Coffee FB

110 cc

Coff. FB

9,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

2,1 gr.

Sugar

5,3 gr.

Chocolate

( 27 )

Chocolate

80 cc

Chocolate

19,0 gr.

Hot Water

60 cc (tot. 140 cc)

Soup *

( 28 )

Soup

150 cc

Soup

8,0 gr.

Hot Water

( 29 )

Hot Water

150 cc

Fresh Brew White

( 31 – 32 – 33 )

Coffee2 FB

110 cc

Coff.2 FB

9,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

1,5 gr.

Sugar

5,3 gr.

Fr. Br. Ex.White

( 34 – 35 – 36 )

Coffee2 FB

110 cc

Coff.2 FB

9,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

2,1 gr.

Sugar

5,3 gr.

Coffee Black

( 37 – 38 – 39 )

Coffee Instant

40 cc

Coffee

1,4 gr.

Sugar

45 cc

Sugar

5,3 gr.

Hot Water

55 cc (tot. 140 cc)

SELECTION

(N.)

WATER DOSES

SUGAR

(to door)

POWDER DOSES

Coffee White

( 41 – 42 – 43 )

Coffee Instant

40 cc

Coffee

1,4 gr.

Milk

60 cc

Milk

1,8 gr.

Sugar

5,3 gr.

Hot Water

50 cc (tot. 150 cc)

Coffee Ex. White

( 44 – 45 – 46 )

Coffee Instant

40 cc

Coffee

1,4 gr.

Milk

60 cc

Milk

3,0 gr.

Sugar

5,3 gr.

Hot Water

50 cc (tot. 150 cc)

Fresh Brew Black

( 47 – 48 – 49 )

Coffee2 FB

110 cc

Coff.2 FB

9,0 gr.

Sugar

60 cc (tot. 170 cc)

Sugar

5,3 gr.

Fresh Brew White

( 51 – 52 – 53 )

Tea FB

110 cc

Tea FB

3,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

1,5 gr.

Sugar

5,3 gr.

Fr. Br. Ex.White

( 54 – 55 – 56 )

Tea FB

110 cc

Tea FB

3,0 gr.

Milk

60 cc (tot. 170 cc)

Milk

2,1 gr.

Sugar

5,3 gr.

Fresh Brew Black

( 57 – 58 – 59 )

Tea FB

110 cc

Tea FB

3,0 gr.

Sugar

60 cc (tot. 170 cc)

Sugar

5,3 gr.

FB Cappuccino

( 61 – 62 )

Coffee FB

80 cc

Coff. FB

6,5 gr.

Milk

55 cc

Milk

8,0 gr.

Sugar

5,3 gr.

Chocolate

30 cc (tot. 165 cc)

Chocolate

3,5 gr.

SELECTION

(N.)

WATER DOSES

SUGAR

(to door)

POWDER DOSES

FB Espresso

( 63 – 64 )

Coffee FB

50 cc

Coff. FB

3,3 gr.

Sugar

60 cc (tot. 110 cc)

Sugar

5,3 gr.

EspressoChoc

( 65 – 66 )

Coffee FB

55 cc

Coff. FB

3,8 gr.

Milk

35 cc

Milk

1,8 gr.

Sugar

5,3 gr.

Chocolate

50 cc (tot. 140 cc)

Chocolate

13,0 gr.

Chocomilk

( 67 )

Chocolate

70 cc

Chocolate

16,0 gr.

Milk

60 cc (tot. 130 cc)

Milk

1,4 gr.

Inst. Cappuccino

( 71 – 72 )

Coffee Instant

40 cc

Coffee

1,6 gr.

Milk

60 cc

Milk

8,0 gr.

Sugar

5,3 gr.

Chocolate

40 cc (tot. 140 cc)

Chocolate

9,6 gr.

Ins.EspressoChoc

( 73 – 74 )

Coffee Instant

40 cc

Coffee

1,4 gr.

Milk

35 cc

Milk

1,8 gr.

Sugar

5,3 gr.

Chocolate

50 cc (tot. 125 cc)

Chocolate

13 gr.

Chilled Water

( 81 )

Still

160 cc

Chilled Water

( 84 )

Carbonated

140 cc

Still

20 cc (tot. 160)

SELECTION

(N.)

WATER DOSES

SUGAR

(to door)

POWDER DOSES

Orange

( 82 )

Still

150 cc

Syrop 1

32 ds

Orange

( 85 )

Still

35 cc

Syrop 1

0 ds

Carbonated

95 cc

Syrop 1

32 ds

Still

20 cc (tot. 150)

Lemon

( 83 )

Still

150 cc

Syrop 2

32 ds

Lemon

( 86 )

Still

35 cc

Syrop 2

0 ds

Carbonated

95 cc

Syrop 2

32 ds

Still

20 cc (tot. 150)

INFORMAZIONI GENERALI.

TABELLA PESI VALIDATORE:

| Linea | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- |
| Peso | 1 | 2 | 10 | 20 | 50 | 5 |

PREZZO SELEZIONI: Tutte le selezioni a 10.00.

NPREZZO SELEZIONI: Tutte le selezioni puntano al prezzo 1.

POSIZIONE PUNTO DECIMALE: 2.

TEMPERATURA CALDAIA EXP: ---- °C.

TEMPERATURA CALDAIA SOLUBILI: 86.0 °C.

RITARDI ACQUE / POLVERI: Ritardo polvere rispetto all’acqua 0.6 sec.

TIPO DI TASTIERA: Tastiera numerica.

LINGUE: Italiano, Francaise, Espanol, English, Deutsch, Danska, Ungaria, Nederlands, Svenska, Czech, Polski e Finnish.

GENERAL INFORMATION.

PAYMENT SYSTEMS DETAILS:

| Line | A | B | C | D | E | F |
| --- | --- | --- | --- | --- | --- | --- |
| Weight | 1 | 2 | 10 | 20 | 50 | 5 |

SELECTION PRICE: All the selections to 10.00.

SELECTION NPRICE: All selections are set price line 1.

DECIMAL POINT POSITION: 2.

TEMPERATURE BOILER EXP: ---- °C.

TEMPERATURE BOILER INSTANT: 86.0 °C.

WATER/POWDER DELAYS: Powder delays to water 0.6 sec.

TYPE OF KEYBOARD: Numerical keyboard.

LANGUAGE: Italiano, Francaise, Espanol, English, Deutsch, Danska, Ungaria, Nederlands, Svenska, Czech, Polski and Finnish.

MODIFICHE.

SW CPU / SCHEDA ATTUAZIONI REV. 1.1:

Modifica alla struttura del database (l’upgrade necessita l’inizializzazione del d.a.).

SW CPU / SCHEDA ATTUAZIONI REV. 1.1 UK:

Introdotta una modifica della gestione del guasto air-break.

Aggiornamento stringhe in inglese.

Modifica del valore minimo del tempo di uscita ugelli per freddo e caldo (80).

Modifica delle attuazioni generate dal pulsante utility “SPOUTS” (uscita e rientro degli ugelli senza arresto)

SW CPU / SCHEDA ATTUAZIONI REV. 1.2:

Aggiunta delle lingue polacca e finlandese.

Modifica delle lingue svedese e danese.

Modifica della gestione delle statistiche (azzeramento) via GSM.

Programmazione tramite l’utilizzo di UP-KEY.

Modifica della gestione dei lavaggi e degli schizzi su distributori con acque fredde.

SW CPU / SCHEDA ATTUAZIONI REV. 1.3:

Eliminazione del controllo della presenza della caraffa in modalità Jug Facilities.

Gestione VENDITA LIBERA con solo sistemi CASHLESS e protocollo MDB.

CHANGES.

SW CPU - I/O BOARD REV. 1.1:

Modification of database structure (upgrade needs the d.a. initialisation)

SW CPU - I/O BOARD REV. 1.1 UK:

Introduction of air-break failure management modification.

Updating of english display messages.

Modification of minimal value for hot and cold spouts movement times (80).

Modification of  movements caused by SPOUTS utility button (spouts outgoing and incoming without stop)

SW CPU - I/O BOARD REV. 1.2:

Insertion of Finnish and Polski languages.

Modified Swedish and Danska languages.

Modified of statistical management by GSM.

D.A. programmation by use of UP-KEY.

Modified washing and spurt management in d.a. with cold water.

SW CPU - I/O BOARD REV. 1.3:

Eliminated jug check during Jug Facilities operation.

Management of free-vend operation with only cashless systems and MDB protocol.